## Slide 1: Computer Aided Diagnostics: A Case Study
Mohammad Haris Baig
Dr. Adnan Khan
Dr. Natasha Nabi
Automated Hepatitis C Detection and Strain Identification From RFLP Gel Images

## Slide 2: Goals
Detecting Hepatitis C
Identifying Hepatitis C Strain

## Slide 3: Objectives
Speed
Accuracy
Reliability
Interactivity

## Slide 4: Goals
Detecting Hepatitis C
Identifying Hepatitis C Strain

## Slide 5: Detecting Hepatitis C
An Image of a G2 Gel

## Slide 6: Labeled Gel Image
A Labeled Image of the Lanes

## Slide 7: Enhancing Contrast
1% Saturation based Enhancement

## Slide 8: Lane Detection
Lane Detection on G2 Image
Results From our Lane Detection Algorithm

## Slide 9: Band Detection
Binarization based on Thresholding

## Slide 10: Band Localization

## Slide 11: Reporting Results
For Each Patient:
For Each Strain:
Matching is based on
Number of Bands Found
Number of Bands Expected
Location of Bands Found
Location of Bands Expected
For Each Patient:
Display Highest Percentage Match Strain Name and Matching Percentage

## Slide 12: Goals
Detecting Hepatitis C
Identifying Hepatitis C Strain

## Slide 13: Hepatitis C Strain Identification
An Image of a DE Digest Gel

## Slide 14: The Problem
To Identify And Match Banding Patterns
In Each Lane to
a Banding Pattern
produced by a Hep-C Strain

## Slide 15: Main Issues
Low Resolution Images
High Degree of Noise
High Degree of Variability in Image Quality
Lack of Standardization of Procedure
Tilted Bands
Smeared Bands / Merged Bands
Broken Bands

## Slide 16: Low Resolution of Images
370 by 98 Pixels
Original Image
- Sample Image for Test
74 by 292 Pixels
Enhanced size
(Loss of Data)
- Left Side Ladder Lane
Notes: If Image Size is Standardized, then our User may not have to enter the Number of Lanes
(A Great Benefit for Batch Processing)

## Slide 17: High Degree of Noise
Notes: Better Quality Images lead to avoiding Issues of handling Noise Reduction and Signal Purification and concentrating on task of Matching.
Also they reduce the burden on the Identification Algorithm

## Slide 18: High Degree of Variability in Image Quality
Sample 2
Sample 1
Notes: High Degrees of Contrast Adjustment to guarantee accurate band detection.

## Slide 19: Lack of Standardization of Procedure
Sample 1
Sample 2
Sample 3
Notes: Leads to Redundancy in Data entry (Big cause of Human Error)

## Slide 20: Tilted Bands
A Problem for Accurate Band Center Detection
Notes: Incorporate Inaccuracy in Model on Detection of Precise location of Bands

## Slide 21: Smeared Bands/ Merged Bands
Notes: Harder Identification of Individual Bands

## Slide 22: Broken Bands

## Slide 23: How to Solve These Problems

## Slide 24: Detecting Lanes

## Slide 25: Detecting Lanes – How to
Too many vertical lines due to Broken Band’s Effects
Notes: What to do about Broken Bands?
Does this suggest an E-M Iterative style algorthim?

## Slide 26: Detecting Lanes

## Slide 27: Detecting Lanes

## Slide 28: Band Detection
Input Image

## Slide 29: Band Detection

## Slide 30: Band Indentification - How to?
Median Based Profile for Each Row
Image Reconstructed from Median Profile

## Slide 31: Band Identification - How to?
Results from Morphological Filtering, Top Hat Filter

## Slide 32: Bands Detection

## Slide 33: Ladder Calibration
Using Pre calibrated Ladder
To interpolate the missing bands

## Slide 34: Reporting Results
For Each Patient:
For Each Strain:
Matching is based on
Number of Bands Found
Number of Bands Expected
Location of Bands Found
Location of Bands Expected
For Each Patient:
Display Highest Percentage Match Strain Name and Matching Percentage
Display Original Image
Display Processed Image with marked bands
Highlight any unusual Bands Found.